### Press Release	August 2022

### MAVOMASTER – MAVOPROBE – MAVOSOFT
The New Light Metering System

GOSSEN Foto- und Lichtmesstechnik GmbH has extended its premium range of light meters to include a versatile light metering system based on 3 components, namely MAVOMASTER, MAVOPROBE and MAVOSOFT.

The MAVOMASTER is a basic universal device that can be combined with various measuring probes. The integrated measuring functions evaluate the measurement results and provide on-site evaluations with the option of saving data in CSV format.  These functions can be assigned to the F1 and F2 function keys as required and include a data logger, a relative measurement, a raster measurement for the assessment of workplace lighting with calculation of Emin, Emax, Eavg, U0 and UD values, a B/A ratio measurement for contrast, a B-A deviation measurement, a %A deviation measurement and an integral measurement for determining the irradiation dose. Key labeling is fluorescent and an optional rubber holster is available for additional impact protection. Measured values can be stored to the 8 GB memory module in CSV format and read out via the USB interface.

The four classified MAVOPROBEs including the LUX 5032 B, the LUX 5032 C, the MONITOR and the LUX / UVA make it possible to measure illuminance and luminance, as well as illuminance and UV-A irradiance at 365 nm. With the latter, GOSSEN is extending its range of applications to the examination of viewing conditions in non-destructive magnetic particle and penetrant testing. Each probe features intrinsic intelligence, can be calibrated individually and transmits its measured values directly to the MAVOMASTER via a serial interface. With the help of the USB adapter, the MAVOPROBE can be connected directly to a PC or a USB hub, and single or multi-channel measuring systems can be set up. Power is supplied via the USB interface with open protocol. When recalibration becomes necessary only the probe needs to be sent in, which significantly reduces shipping costs.

Intuitive MAVOSOFT software supports one or more MAVOMASTERs and MAVOPROBEs. It handles device control and data communication, as well as visualization and logging of the measured values. Data export as a CSV file permits further universal processing of the measured values in Microsoft Office products.

Detailed information concerning the MAVOMASTER light metering system can be found on GOSSEN’s website at www.gossen-photo.de.

Images:

Further information:

GOSSEN Foto- und Lichtmesstechnik GmbH, Lina-Ammon-Str. 22, D-90471 Nuremberg

Klaus-Peter Richter, phone: +49 911 800621 10, e-mail: klaus-peter.richter@gossen-photo.de