### Press Release	August 2022

### MAVOPAD
Universal Flicker Meter for PstLM and SVM

GOSSEN Foto- und Lichtmesstechnik GmbH has extended its premium range of light meters to include a universal flicker meter for SVM and PstLM.

With the advent of LED technology in the field of lighting, flicker measurement is becoming increasingly important because LEDs respond very quickly to voltage fluctuations, thus resulting in fluctuating brightness, i.e. flicker. Flicker influences human health and mood, and our sense of well-being. It can trigger epileptic seizures, migraine headaches, fatigue, restricted visual acuity, distraction and impaired vision. In the case of rotating objects, the strobe effect results in incorrect evaluations and accidents.

Previous time range parameters such as flicker percentage, flicker index and flicker frequency are no longer sufficient, which is why new calculation methods and parameters have been developed that take this frequency range into account. These include PstLM and SVM, whose importance has increased due to the establishment of limit values in EU ecodesign requirements for light sources and separate industrial measuring instruments. Flicker assessments in accordance with IEEE 1789 and ASSIST Mp are used outside of Europe.

The universal MAVOPAD supports all of these calculation methods and parameters for flicker, and is open for further complex evaluation methods. In addition to displaying the parameters, the time curve and the frequency spectrum are also depicted. High 16-bit resolution and a fast sampling rate of up to 1.6 MHz even make it possible to detect lighting dimmed at a high PWM frequency.

The highly accurate MAVOPAD is ideally suited for laboratory and development applications and is indispensable for manufacturers and importers of lamps, luminaires and LED control gear in order to verify or check for compliance with the specified EU limits. By the same token, the MAVOPAD is used in the field for the inspection of installed lighting systems. Measurement data can be stored to internal data memory in CSV format and read out via the USB interface.

Detailed information concerning the universal MAVOPAD flicker meter can be found on GOSSEN’s website at www.gossen-photo.de.

Images:

Further information:

GOSSEN Foto- und Lichtmesstechnik GmbH, Lina-Ammon-Str. 22, D-90471 Nuremberg

Klaus-Peter Richter, phone:  +49 911 800621 10, e-mail: klaus-peter.richter@gossen-photo.de